## Slide 1
PROJECTED BY – AVISHIKTA DASH
Roll – 2206
Department of Nutrition,
B.Voc Food Processing 6th semester
Guide – APURBA GIRI¹ &
AYAN MONDAL²
HEAD OF ASSISTANT PROFESSOR¹
ASSISTANT PROFESSOR²
(DEPT. OF NUTRITION)
Mugberia Gangadhar Mahavidylaya
Mugberia Gangadhar Mahavidylaya
PROJECT ON ENTREPRENEURSHIP
DEVELOPMENT OF DIABETIC CANNED RASGULLA PLANT

## Slide 3
CONTENTS
INTRODUCTION
MARKET DEMAND
AREA
INVESTMENT
LISENCE
PRODUCTION
RAW MATERIALS
MACHINARY
FLOW CHART
LAYOUT
PACKAGING
MAN POWER
EQUIPMENTS DETAILS
SUPPLY
PRODUCT DETAILS
PRICE & QUANTITY
SHELF LIFE
MARKET STRATEGIES
SALARY
PROFIT

## Slide 4
Rasgulla or Roshogolla is an Indian syrupy sweet. The product is perishable. However, we can store canned rasgulla for a longer period. Here in this article, we intend to explore how to start a canned rasgulla making business.
Any individual can start a canned rasgulla making business with moderate capital investment. Additionally, revenue-wise the business is lucrative and highly profitable. However, you must ensure a regular supply of fresh milk to your factory.
In India, K. C. Das first started preparing canned rasgulla. And the product got the immediate popularity even abroad. Nowadays, you can find several brands of this item. This sweet item is popular throughout the country.
INTRODUCTION

## Slide 5
MARKET DEMAND
Rasgulla is very popular, especially in West Bengal, Bihar, Odisha, and North India. Its popularity is also growing up in South India. Canned rosogolla has more demand because it is more hygienically prepared and has a longer shelf life.
A major number of sweets shops do not produce items of their own. Generally, they outsource the item from reliable manufacturers. So you can sell fresh rasgulla to them. However, you must concentrate on the canned form. And this value-added item has more revenue potential compared to a fresh one.
It is seen that canned form makes transportation easier. And the product has good export potential. The major importing countries are Bangladesh, Nepal, Australia, Canada, the USA, Hong Kong, New Zealand, Malaysia, Singapore, etc.

## Slide 6
AREA & LOCATION
Land & Building – Area 1200-1500 sq. ft.
INVESTMENT
REGISTRATION & LISENCE
In starting this business, you will need to apply for business registration and different licenses. Here we put some of the basic considerations. However, it is advisable to check your local state law.
First of all, decide on a form of organization and register your business with ROC.
Secondly, you must obtain a Trade License from the Municipal Authority.
Compliance with the PFA Act is mandatory. Apply for an FSSAI license as the business comes under the packaged food industry.
Apply for BIS Certification. Maintain quality standard specification IS 4079:1967.
Apply for GST registration number.
If you want to export the item, you must obtain an IEC license.
Additionally, you can protect your brand name by Trademark registration.
This business doesn’t attract pollution issues. However, check with your local PCB office.
Total Capital Investment Rs. – 26 Lacks.
Land & Building Rs. – 8 Lacks.
Machinery Rs. – 9 Lacks.
Raw materials, labour cost and others Rs. – 9 Lacks.

## Slide 7
PRODUCTION
RAW MATERIALS
Skim milk (0.1% fat, 8.9% SNF & 0.17% acidity)
Citric acid
Sucralose
Sodium alginate
MACHINARY
Stainless Steel tank
Boiler
Milk weighing balance
Kneader
Automatic can sealer
Testing equipment
LAB TESTS
Fat test
Protein test
Quality test

## Slide 8
Serial No. | Equipments Name | Number | Cost
Production equipment's |  |  | 
01. | Stainless steel jacketed tank | 1 | 50,000
02. | Plate heat exchanger | 1 | 7,500
03. | Boiler | 1 | 15,500
04. | Milk weighing machine | 2 | 10,418
Quality control & testing equipment's |  |  | 
05. | Protein analyzer | 2 | 1,50,000
06. | Butyrometer | 2 | 160
Packaging equipment's |  |  | 
07. | Automatic can sealer machine | 1 | 63,299
Distribution equipment's |  |  | 
08. | Truck | 1 | 6,00,000
Total: |  |  | 8,96,877
EQUIPMENTS DETAILS

## Slide 9
FLOW CHART OF DIABETIC RASGULLA
Cow milk
Citric acid added
Heating 80°c
Heating to boiling point
Cooling/coagulation to 80°c
Holding coagulation mass for 10-15min
Strain
Whey
Dripping of whey(30-45min)
Channa
Sucralose sweet syrup cheese ball formation(Rasgulla)
Cooking in sucralose solution (18%) for 20-30 min soaking in 16% sucralose solution
Kneading and ball formation
Boiling of water (100°c)
Added sodium alginate (1.67%)
Added of sucralose (18%)(20-30 min boiling)
Preparation of soaking syrup(16%)
FLOW CHART OF SOAKING SYRUP

## Slide 11
PACKAGING
MAN POWER
12 Labours(11 Ladies & 01 gents)
4 Labours (Processing section)
2 Labours (Packaging section)
2 Ladies (Lab)
2 Labours(Store section)
1 Ladies & 1 Gents(security guard)
Metals such as steel and aluminum are used in cans and trays. It also is used in trays and for wraps such as aluminum foil, which provide an oxygen and light barrier. It is lighter in weight than steel and resists corrosion.
SUPPLY
Online
Offline

## Slide 12
SHELF LIFE
Best before 6 months from date of packaging.
After opening refrigerate and consume within 1-2 days
PRODUCTS DETAILS
500gm(pieces: 10)
700gm(pieces: 15)
1kg(pieces: 20)
PRICE & QUANTITY
Objective | 500 gm | 700 gm | 1 kg
Raw materials | 50 | 110 | 150
Can | 25 | 40 | 45
Labels | 12 | 25 | 30
Water | 13 | 22 | 25
Electricity | 15 | 20 | 23
Labour | 20 | 50 | 90
Cartoons | 15 | 20 | 25
Others | 20 | 23 | 12
Size of cans | Total cost | Wholesaler cost | MRP | Profit
500gm | 170 | 200 | 250 | 30
700gm | 310 | 350 | 400 | 40
1kg | 400 | 450 | 500 | 50

## Slide 13
MARKET STRATEGIES
SALARY
PROFIT
Digital marketing
Advertising
Direct marketing
Restaurants
Shopping complex
Social media(like- flipkart, amazon, big basket, food mart etc.)
Salary per worker – 8k
Lab assistand – 10k
Depending on production

## Slide 14
Name Of The Plant
AVIRAJ CANNED SWEETS
“I AM SO SWEET, BUT NOT HARMFUL TO YOU”
HOW TO DO BRANDING FOR MY DIABETIC CANNED RASGULLA PRODUCT?
Register an easy and catchy name to remember the name for product branding. Add product brand name, product description, logo, content, net weight and preparation ingredients on the can.